## Slide 1: Background: DWR’s UWMP data
In California, water suppliers that provide more than 3,000 acre-feet of water annually or serve more than 3,000 customers (referred to as urban water suppliers) are required to prepare a UWMP every five years and submit those plans to the California Department of Water Resources (DWR).
The first UWMPs were published in 1990.
The UWMPs contain past and projected future water demand for the supplier’s service area. While utilities may develop and publish demand forecasts in other documents, the projections in the UWMPs allow for a consistent evaluation across California’s urban water suppliers.

## Slide 2: Accessing DWR’s UWMP data
Website: https://water.ca.gov/Programs/Water-Use-And-Efficiency/Urban-Water-Use-Efficiency/Urban-Water-Management-Plans
Historic UWMPS from 2000 to 2015 are available in a PDF format on the website
  Scroll to the bottom of the website and select the tab for ‘Historic’ to access these files
To access 1990 and 1995 UWMPs, you typically must submit a Public Records Request
From 2015 onwards, data tables are available in electronic format, easily downloadable excel spreadsheets here: https://wuedata.water.ca.gov/

## Slide 3: Relevant tables for demand forecasting
Tables for historical data are not typically available though charts may be available in most UWMPs.
Most relevant tables in the UWMP for demand/supply forecasting:
  Table 3-1 Retail: Population - Current and Projected
  Table 4-1 Retail: Demands for Potable and Raw Water – Actual
  Table 4-2 Retail: Demands for Potable and Raw Water – Projected
  Table 6-4 Retail: Current and Projected Recycled Water Direct Beneficial Uses Within Service Area
  Table 6-8 Retail: Water Supplies - Actual
  Table 6-9 Retail: Water Supplies - Projected

## Slide 4: Tips when using UWMP data
Check numbers reported to DWR with numbers published in the UWMP
  If you don’t have access to information that was directly provided to DWR, check for consistency between information published in the UWMP report and information in the electronic data tables on the public data portal.
Check how recycled water is handled in the supplier’s demand and supply estimates (sometimes it is excluded, sometimes it is included). It is best to include it but at least be consistent.
Ensure consistent end-use categories (e.g., residential, CII, distribution leaks) are reported when comparing across different suppliers and/or different years.
Check for data outliers (and reporting errors). For example, filter largest to smallest values and check to see if a value is significantly larger or smaller than expected.

## Slide 5
For feedback or questions, please contact
Heather Cooley hcooley@pacinst.org
Sonali Abraham sabraham@pacinst.org